HYDROFLUOSILICIC (HFS) ACID

TECHNICAL SPECIFICATION

1.	GENERAL REQUIREMENT

1.1	General:  The intent and purpose of this specification document (the “Specification”) is for the Contractor to furnish and deliver liquid Hydrofluosilicic Acid (a.k.a. “HFS”) (23 Percent By Weight H2SiF6) FOB destination in accordance with the American Water Works Association’s (AWWA’s) Standard B-703-11 for fluoride, except as modified or supplemented herein, to the Busytown Water Utilities Department.  Deliveries may be made by either “bulk” or tanker deliveries or “non-bulk” or flatbed truck deliveries (both as defined in Paragraph 5).

1.2	Award:  Award will be made to the lowest responsible and responsive bidder(s) meeting the Specification; price, product quality, safety record, previous performance, reliability and other factors to be considered.  Busytown will not be responsible for any transactions between the successful bidder(s) and any public entity that may elect to utilize this bid.  At its sole discretion, Busytown may award separate contracts for the “bulk” and “non-bulk” HFS deliveries.

##### 2.	BIDDER QUALIFICATION / SUBMITTALS

2.1	Definition:  For purposes of this Bid, the term “Bidder” shall be defined as the company submitting a bid to Busytown and shall include all subsidiaries, affiliates, and subcontractors.  As such, any requested documentation shall apply to all subsidiaries and affiliated companies as well as any subcontractors.  In the event that a company is using a subcontractor to either manufacture or deliver the product, the requested items (e.g., references, terminations, and safety incidents) shall apply to the subcontractor as well.

2.2	Bid Sample:  Each prospective Bidder shall submit a 1000-ml sample of their product representative of their manufacturing process from Bidder’s manufacturing facility which would serve the customer to a third party testing laboratory for analysis within the past ninety (90) days.  The laboratory shall ascertain whether the Bidder’s product is in compliance with this Specification for % H2SiF6, % Arsenic, % Heavy Metals (defined as lead), color, clarity and specific gravity.  The cost of the analysis shall be borne by Bidder.  The results of the analysis shall be submitted with the Bidder’s proposal.  Failure to submit a sample or meet the requirements of the Specification shall result in Bidder being disqualified.

2.4	Other Samples:  Further, Busytown reserves the right to take samples from Bidder’s other customers to ensure that the Bidder’s sample and delivery equipment is in compliance with all the requirements of this Specification and such a sample shall be judged representative of the Bidder’s quality.  The Bidder shall provide a customer contact and phone number at a nearby utility whereby Busytown may obtain sample of Bidder’s product to check it for compliance with the Specification.  Notwithstanding the foregoing, Busytown may choose to obtain a sample this customer or from any of Bidder’s customers to ensure compliance with the Specification.  In such event, Busytown shall bear the cost of any analysis.  Based on this compliance check, failure to meet the requirements of this Specification shall result in Bidder being disqualified.

2.4	References:  Each prospective Bidder shall submit a list of at least five (5) references to include phone numbers that use or have used its HFS at its water treatment plant(s) in the past three years.  The Reference List shall list actual users at the water plants and not purchasing agents.  Additionally, each Bidder shall provide the names of any customers where its contract was terminated early (e.g., debarred) for safety, quality, or service issues for any product it supplies over the past five years.  The Bidder shall also provide a detailed listing any governmental contracts in Florida where it failed to make deliveries when requested, declared Force Majeure with regard to delivery or pricing on any contract or claimed that there was a shortage of product and failed to make a delivery when requested or prematurely ended a contract (e.g., “failure to deliver”).  Busytown intends to do a reference check and utility survey to ascertain the veracity of the Bidder’s submittal.  Failure to disclose references, terminations, or failure to deliver will result in Bidder being disqualified from bidding on this product.

2.5	Safety and Reliability:  As part of assessing the Bidder’s reliability and safety record, the Bidder shall submit a copy of its OSHA Form 300A/300 logs for the past three years (if the Bidder utilizes a third party driving company or affiliated company, then they shall submit the OSHA 300 logs for that company as well).  Additionally, the Bidder shall also submit a recent printout in the last thirty (30) days from the USDOT website www.safersys.org which was established for prospective customers to check the driving safety record of prospective contractors.

##### 3.	COMMERCIAL CONDITIONS

3.1	Term:  The initial term of the contract for the HFS shall be for one (1) year (“Initial Term”) with up to two (2) one-year renewal periods.  Each of the renewal periods is subject to mutual agreement and approval by both Busytown and the Contractor.  The effective date of service under this supply agreement shall be approximately [Fill in Date].

3.2	Pricing:  All pricing shall be in terms of a price per gallon (freight prepaid FOB to each Busytown facility).  The price of the HFS shall be fixed for the Initial Term of this agreement and shall not be subject to any price escalation or fuel surcharges (the “Base Price”).   If the parties agree to renew the agreement, Busytown may consider a price increase in either of the renewal years based on verifiable changes in the marketplace.

3.3	Payment Terms:  NET 30 days.

##### 4.	DELIVERY REQUIREMENTS

4.1	Contractor shall make “normal” deliveries within four (4) calendar (i.e., not “working” days) days after receipt of order and must make “emergency” deliveries within 24 hours.  An emergency delivery is defined as a delivery which is necessary in order to prevent Busytown from running out of HFS in less than 24 hours.  Busytown shall endeavor to minimize the number of “emergency” deliveries.

  - All deliveries of liquid HFS shall be freight prepaid, F.O.B. to each Busytown facility.

  - Delivery time of day shall be arranged upon placement of order.   Deliveries made to unmanned facilities must be coordinated with Busytown so the driver can gain access to the facility.

  - All deliveries of liquid HFS shall be made by properly cleaned carrier tank truck to the locations specified in paragraph 5 below.

  - Packaging and shipment of liquid HFS shall conform to all current regulations of the State of Florida, the United States Department of Transportation and all other applicable regulatory agencies.

  - All delivery personnel must have company cell phones to facilitate deliveries to unmanned and manned facilities.  Experience has shown this to be critical to effective coordination of deliveries to the various Busytown facilities.

  - Busytown reserves the right to change quantities and delivery dates at its discretion with a 24-hour notice.

  - The Contractor shall be responsible for pumping liquid HFS into the storage tanks at the delivery sites and shall provide all necessary hoses, fittings, air-padding, pumps, etc. required to safely and efficiently “offload” the liquid HFS into designated storage tanks.  Contractor shall be responsible for ascertaining the correct storage tanks and fill point locations to prevent accidental discharge of the product into the wrong storage tank(s).

  - The Contractor shall be responsible for any spills resulting from the failure of its or its subcontractor’s delivery equipment or from failure of attendant delivery personnel in the proper performance of their duties.  Proper performance shall require attendant delivery personnel’s constant inspection and observation of unloading operations and knowledgeable response to problems or emergencies, which would most commonly be expected to occur.  Busytown reserves the right to refuse any and all deliveries made with equipment that is poorly maintained and/or leaking HFS.

  - The tanks or trailers shall be clean and free of residue that may contaminate the Contractor’s product or impede the unloading process.  It is the Contractor’s responsibility to verify the cleanliness of the transporting equipment before loading.  All appurtenant valves, pumps, and discharge hoses used for the delivery of HFS shall be supplied by the Contractor and shall be clean and free from contaminating material.  Busytown may reject a load if the equipment is not properly cleaned.  Contractor shall furnish Busytown an approved, leak-free connection device between the trailer and its intake receptacle.  The Contractor shall observe the entire filling operation at each delivery site and shall immediately report any spills caused during the filling operations.  The Contractor shall take immediate and appropriate actions to clean up any spilled liquid HFS.  If the spill is not cleaned up, Busytown will hire a certified hazardous material handling company to clean up the spill, and the cost of such service will be charge to the Contractor and deducted from the amount due to the Contractor.  If Busytown’s unloading equipment such as pipe, valves or level indication and alarms should fail and the spillage is not the fault of the Contractor or its subcontractor, the Contractor shall be relieved of cleanup of the spill.

  - Because of security and safety concerns, all delivery vehicle drivers shall be U.S. citizens and have a proper commercial driver’s license with a Hazardous Material endorsement.  Contractor’s drivers shall display its driver’s license and whenever challenged by Busytown during the delivery.  Failure of a Contractor’s driver to show proper license to Busytown shall result in rejection of delivery and subsequent possible termination of the Contractor’s supply agreement.

  - Delivery Shipments shall be rejected which fail to meet any of the requirements of the Specification.  In the event a delivery shipment is rejected, upon notification to the Contractor that the shipment is rejected, Contractor shall be required to ship a replacement delivery to the affected location within four (4) hours from time of notification.  Failure to provide replacement product that meets the Specification within the specified time period will constitute failure to comply with the delivery requirements set forth in this document.

##### 5.	DELIVERY LOCATIONS

  - Delivery sites and quantities are subject to deletions or additions as necessary to meet the water production demands of Busytown.

  - Split deliveries to multiple locations will be coordinated and accepted by Busytown, when possible, to encourage economical delivery of product via bulk tankers dependent on storage capacities at time of delivery.  However, Bidder should note the Minimum Delivery requirement for each item and be prepared to deliver this quantity when required at no additional cost.

  - Liquid HFS consumption at each location is an estimate only and Busytown shall not be bound by these amounts in its contract with Contractor.  In FY 2XXX, Busytown projects to use XXX,XXX gallons of HFS.

  - Delivery Locations:

| LOCATIONS | STORAGE CAPACITY | ESTIMATED ANNUAL QUANTITY |
| --- | --- | --- |
| Busytown WTP #1 100 Main Street Busytown, USA | X -X,XXX GALLONS | XX,XXX GALLONS |
| Busytown WTP #2 100 Main Street Busytown, USA | X – X,XXX GALLONS | XX,XXX GALLONS |
| Busytown WTP #3 100 Main Street Busytown, USA | X - X,XXX GALLONS | XX,XXX GALLONS |

###### 6.	PRODUCT MATERIAL REQUIREMENTS

  - HFS supplied under this contract shall be tested and certified as meeting the Specification, the AWWA Standard B703-11 and those of the American National Standards Institute/National Sanitation Foundation Standard 60 (ANSI/NSF Standard 60), Drinking Water Treatment Chemicals Health Effects.

  - It is the responsibility of the Contractor to inform Busytown that its NSF or UL certification has been revoked or lapsed within 24 hours of the time the supplier receives verbal or written notification.  Loss of certification shall constitute sufficient grounds for immediate termination of the contract between Busytown and Contractor.

  - Liquid HFS delivered under this Specification shall have a minimum concentration of 23% by weight H2SiF6 as determined by chemical analysis.  Busytown reserves the right to test specific gravity to make this determination or send to an outside third-party laboratory to do a more detailed analysis.

  - Product shall be a clear water white liquid with no visible cloudiness, impurities, or sediment and shall have less than 20 units of color.  It shall contain no soluble materials or organic substances in quantities capable of producing deleterious or injurious effects on the health of those consuming water treated with the liquid HFS.  Busytown shall obtain a sample in a clear graduated cylinder prior to offloading from Contractor.  Any yellow or brown caste shall result in immediate rejection of the load.

  - Liquid HFS delivered under this Specification shall have a minimum specific gravity of 1.19 and a maximum specific gravity of 1.22.

  - Liquid HFS delivered under this contract shall meet the following containment concentration limits:

Arsenic				< 5.0 ppm

Heavy Metals			< 100 ppm as Pb

Color					< 10 Units

###### 7.	QUALITY ASSURANCE, SAFETY AND TRAINING

  - Sampling and Testing

    - All Sampling and Testing shall be in accordance with EPA and AWWA B703-11 standards.

    - Sampling and Testing Prior to Unloading:  The Contractor’s delivery trailer shall have a sample port to provide a sample for analysis.  At the sole discretion of Busytown, the Contractor’s delivery personnel (driver) may be asked to provide a sample of liquid HFS before the shipment is unloaded.  Busytown will supply the sample container and the driver shall collect the sample from the tank truck and turn it over to Busytown.  The sample shall be considered representative of the lot.  Busytown reserves the right to subject samples of the liquid HFS to quick analyses to ensure that it meets basic conditions of the specification with respect to specific gravity, weight percent of H2SiF6, arsenic, heavy metals and suspended solids (i.e., clarity).   Any lot tested by Busytown that fails to comply with the Specification shall constitute grounds for rejection of that lot.   No payment shall be made for HFS that is rejected.  The Contractor or its subcontractors shall allow 60 minutes for this testing to be completed.  If testing can not be completed within the 60-minute period, Busytown shall allow the Contractor to unload the shipment.  In the event that the load is rejected, the Contractor shall have four (4) hours to supply another shipment.  In the event that the Contractor is unable or unwilling to supply another shipment within this time period, Busytown has the right to procure a shipment from another source and this will failure to deliver shall constitute a second rejection.  Three rejections of a lot or shipment during any period of this contract shall constitute automatic termination of the Contractor’s supply contract with Busytown.

    - Sampling and Test of Shipment After Unloading.  Busytown reserves the right to subject samples of the liquid HFS to complete analyses to ensure that it meets EPA specifications, AWWA B703-11 specifications, and the Specification.   Three failures during any period of this contract shall constitute automatic termination of the Contractor’s supply contract with Busytown.

    - Certified Analysis.  Contractor shall supply an affidavit, signed by a corporate designated official, certifying that the liquid HFS furnished by the Contractor, complies with all applicable requirements of this Specification and AWWA Standard B703-11, latest revision.

7.2	Manufacturer’s Laboratory Delivery Reports

    - A certified report from the manufacturer shall be submitted for each liquid HFS delivery to Busytown.

    - The  report shall contain the following data:

- Date and Time of Manufacture

- Percent by Weight H2SiF6

- Specific Gravity  (Referenced to a temperature)

- Suspended Solids (Clarity)

    - No deliveries will be accepted by Busytown unless accompanied by said certified laboratory report for the specific batch of liquid HFS delivered showing the above data and that it conforms to the Specification.   Regardless of whether at different delivery sites, failure to comply with this provision three (3) times during the contract period shall constitute sufficient grounds for termination of the contract between Busytown and Contractor.

7.3 	Quarterly Reports

7.3.1	At the start of the contract and thereafter each quarter, Busytown shall utilize one of the approved testing agencies listed in this Specification to analyze a sample of the liquid HFS delivered to Busytown.  The Contractor shall supply the sample container and the driver shall collect the sample from the tank truck.  This sample will be given to Busytown at the time of the sample and Busytown shall “chill the sample” and then forward it to the approved authorized testing agency.  Any failure to comply with the Specification shall constitute grounds for cancellation of the contract between Busytown and Contractor.  The cost of such testing shall be paid by the Contractor and this cost should be included in the Contractor’s bid price.

###### 8.	OCCUPATIONAL HEALTH AND SAFETY

  - Contractor Safety Requirements

    - Contractor must ensure delivery personnel’s compliance with all OSHA requirements, including personal protective equipment for Contractor delivery personnel, including without limitation chemical goggles, transparent face shield and hard hat, rubber gloves, rubber boots, and rubber or plastic-coated fabric apron or slicker suit.  Contractor delivery personnel must wear at minimum, chemical goggles and rubber gloves when handling hoses and valves.

    - Contractor delivery personnel must remain within a safe proximity while the transfer is in progress and continuously monitor for leaking hoses, connections, or other problems.  It is the responsibility of Contractor delivery personnel to contain leaks and to report any and all spills.

  - Safety Data Sheets.  In compliance with Chapter 442 Florida Statutes, any chemical delivered form a Contractor, must be accompanied by a Safety Data Sheet (SDS).  The SDS must be maintained by the user agency and must include the following information:

- The Chemical Name and the common name of the toxic substance

- The hazards and other risks in the use of the toxic substance, including:

- The potential for fire, explosion, corrosivity and reactivity;

- The known acute and chronic health effects of risks from exposure, including the medical conditions which are generally recognized as being aggravated by exposure to the toxic substance; and

- The primary routes of entry and symptoms of overexposure.

- The proper precautions, handling practices, necessary personal protective equipment, and other safety precautions in the use of, or exposure to, the toxic substances, including appropriate emergency treatment in the case of overexposure.

- The emergency procedure for spills, fire, disposal and first aid.

- A description, in lay terms, of the known specific potential health risks posed by the toxic substance intended to alert any person reading this information.

- The year and month, if available, that the information was complied and the name, address, and emergency telephone number of the manufacturer responsible for preparing the information.

- Any questions regarding this requirement shall be directed to:

Department of Labor and Employment Security

Bureau of Industrial Safety and Health

Toxic Waste Information Center

2551 Executive Center, Circle West

Tallahassee, Florida  32301-5014

Phone:  800/367-4378

8.3	Emergency Plan of Action and Safety Training

    - Within 30 days of award and acceptance of the contract for the supply of liquid HFS, the Contractor shall provide in writing, an emergency contingency plan, with appropriate telephone contacts, for Busytown to follow in case an emergency supply of liquid HFS is needed.  The Contractor shall supply in writing, an emergency spill response plan with appropriate emergency response personnel names (to include at least two degreed engineers who live within one hundred fifty miles of Busytown) and telephone contact numbers (24-hour contact numbers) within 30 days of award and acceptance of the contract to supply liquid HFS.  In addition, the proper spill response notification procedure, along with any forms required by all local, state or federal regulatory agencies, shall be supplied by the Contractor.  This section in no way relieves the Contractor of his responsibility to notify the proper regulatory agencies in the event of a spill incident.  In the event of a spill or leak, the Contractor shall supply the necessary personnel (including one degreed engineer) to immediately respond to such an event, to work with the local Hazardous Materials Response Team and to manage and oversee “After Event” cleanup efforts.  Should a spill or leak occur, caused by Contractor’s personnel, equipment or method of delivery, Contractor shall immediately comply with all applicable terms and conditions of the current version of Title III, Superfund Amendments and Reauthorization Act of 1986, 42 U.S.C.S.  11001, et seq. (SARA) and the Florida Hazardous Materials Emergency Response and Community Right to Know Act of 1988, Chapter 252, Part II, Florida Statutes.  The responsibility for compliance with Federal and State rules and regulations regarding Contractor caused spills or releases shall be the sole responsibility of Contractor.  The Contractor shall indemnify and hold Busytown harmless for any failure to properly report and /or comply with this provision.  In addition, Contractor shall bear all expenses of spills, unless caused by the sole negligence of Busytown.

    - Safe Handling Training.  The Contractor shall provide an appropriate safe handling training course for liquid HFS within the first month of the contract, to all current Busytown operations personnel and shall be available to conduct “refresher” courses or new employee training at six (6) month intervals during the contract period.  The Contractor shall provide this assistance at no charge to Busytown.

    - Technical Assistance.  The Contractor shall provide engineering and technical assistance, as needed, regarding the application of its product and disposal and handling of residues and sludge’s produced by the application of liquid HFS in the water and wastewater treatment process.  This expertise shall extend to the application of all other chemicals used by Busytown in its water treatment and wastewater treatment plants.  The Contractor shall provide this assistance at no charge to Busytown.

###### 9.	TERMINATION

In addition to the various statements in this Specification stating the grounds for automatic termination of the Contractor’s contract to supply liquid HFS to Busytown, and in addition to any other remedies, including the right to obtain cover and charge Contractor for the costs of cover.  “Cover” is defined as the right of Busytown to obtain a replacement product from another source in the event that the Contractor is unable to supply product in accordance with the Specification and the Contractor pays the cost difference, if any, between its contracted price and the price Busytown paid for the replacement product.   Contractor’s failure to comply with this Specification three (3) times over the duration of this contract shall constitute sufficient grounds for termination of the contract by Busytown.  These failures any three of which can result in termination of the contract, include, but are not limited to, failure to deliver in a timely manner, failure to deliver with proper equipment, failure of the liquid HFS to meet the Specification at anytime, failure to provide a certificate of analysis, failure to comply with the safety and OSHA requirements of the Specification, failure to provide drivers with company cell phones, failure to provide requested technical assistance and/or training and failure to respond in a timely manner to any Busytown emergency related to the supply of this product.

###### 10.	BIDDER’S CHECKLIST (MUST BE TURNED IN WITH BID)

- Pricing Information

HFS (23% +/-.5% H2SiF6) Deliveries

Price Per Gallon:						$ ___________ / gallon

- Third Party Laboratory Analysis of HFS Sample			  	Y/N

- NSF-60 Sample Results for Past Two Years				Y/N

- List of Sites that Busytown can Pull a representative sample	Y/N

- List of References (Five)							Y/N

- List of Subcontractors or Affiliates						Y/N

- List of “Failure to Deliver” Incidents (Last Five Years)			Y/N

- List of Terminations/Debarments (Last Five Years)				Y/N

- Copy of OSHA Form 300A/300 logs (Last Three Years)			Y/N

- USDOT Driving History Included						Y/N

- Other Information on Company						Y/N

- Any Exceptions Taken to the Specification  (Any of which may result in Bidder’s disqualification) 									Y/N

I certify to the best of my knowledge and hereby attest that the above listed information submitted with my company’s proposal is accurate.  I understand that submission of any false or misleading information or failure to submit required information for any product we sell shall be grounds for my proposal to be disallowed and not considered.

_________________________________________________________________________

Name of Bidder

_________________________________________________________________________

Address of Bidder

_______________________________________________________	______________

Signature and Title of Authorized Representative					Date